## Slide 1
录
实
目
项
《华为eNSP网络设备配置》
10.3.3 IPsec VPN配置实例

## Slide 2
10.3.3 IPsec VPN
3． IPSec VPN配置实例
例1 如图10-6所示，现欲在北京总公司与上海分公司之间建立 IPSec VPN 隧道，分别在R1和R2完成配置，使192.168.1.0/24与192.168.2.0/24之间的通信使用安全隧道穿越Internet，IP地址规划如图10-6所示。

## Slide 3
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（1）配置基本信息，包括路由器主机名、IP地址及静态路由。
#配置R1基本信息
<Huawei> system-view
[Huawei] sysname R1 //配置路由器的名称为R1
[R1] interface GigabitEthernet 0/0/0
[R1-GigabitEthernet0/0/0] ip address 192.168.1.254 24 //配置端口IP
[R1-GigabitEthernet0/0/0] interface GigabitEthernet 0/0/1
[R1-GigabitEthernet0/0/1] ip address 11.0.0.1 24
[R1-GigabitEthernet0/0/1] quit
[R1] ip route-static 12.0.0.0 255.255.255.0 11.0.0.2 //配置静态路由
[R1] ip route-static 192.168.2.0 255.255.255.0 12.0.0.2

## Slide 4
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（1）配置基本信息，包括路由器主机名、IP地址及静态路由。
#配置Internet基本信息
<Huawei> system-view
[Huawei] sysname R1 //配置路由器的名称为Internet
[Internet] interface GigabitEthernet 0/0/0
[Internet-GigabitEthernet0/0/0] ip address 11.0.0.2 24 //配置端口IP
[Internet-GigabitEthernet0/0/0] interface GigabitEthernet 0/0/1
[Internet-GigabitEthernet0/0/1] ip address 12.0.0.1 24
[Internet-GigabitEthernet0/0/1] quit

## Slide 5
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（1）配置基本信息，包括路由器主机名、IP地址及静态路由。
#配置R2基本信息
<Huawei> system-view
[Huawei] sysname R2 //配置路由器的名称为R2
[R2] interface GigabitEthernet 0/0/0
[R2-GigabitEthernet0/0/0] ip address 192.168.2.254 24 //配置端口IP
[R2-GigabitEthernet0/0/0] interface GigabitEthernet 0/0/1
[R2-GigabitEthernet0/0/1] ip address 12.0.0.2 24
[R2-GigabitEthernet0/0/1] quit
[R2] ip route-static 11.0.0.0 24 12.0.0.1 //配置静态路由，子网掩码24位
[R2] ip route-static 192.168.1.0 24 11.0.0.1

## Slide 6
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（2）定义各自要保护的数据流
#R1定义要保护的数据流ACL
[R1] acl 3001 //配置高级acl，编号3000--3999
[R1-acl-adv-3001] rule 5 permit ip source 192.168.1.0 0.0.0.255 destination 192.168.2.0 0.0.0.255 //规则5，允许源192.168.1.0/24访问目标192.168.2.0/24
[R1-acl-adv-3001] quit
#R2定义配置R2要保护的数据流ACL
[R2] acl 3001
[R2-acl-adv-3001] rule 5 permit ip source 192.168.2.0 0.0.0.255 destination 192.168.1.0 0.0.0.255
[R2-acl-adv-3001] quit

## Slide 7
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（3）创建IPSec安全提议
#R1创建IPSec安全提议。IPSec安全值串为1,方便记忆。
[R1] ipsec proposal 1 //IPSec安全提议名称,也可取值串1-15
[R1-ipsec-proposal-1] esp authentication-algorithm sha2-256
[R1-ipsec-proposal-1] esp encryption-algorithm aes-128
[R1-ipsec-proposal-1] quit
#R2创建IPSec安全提议，与R1配置一致。
[R2] ipsec proposal 1
[R2-ipsec-proposal-1] esp authentication-algorithm sha2-256
[R2-ipsec-proposal-1] esp encryption-algorithm aes-128
[R2-ipsec-proposal-1] quit

## Slide 8
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（4）创建IKE安全提议
#R1创建IKE安全提议
[R1] ike proposal 1 //IKE安全提议名称,取值1-15
[R1-ike-proposal-1] encryption-algorithm aes-cbc-128 //密钥加密算法
[R1-ike-proposal-1] authentication-algorithm md5 //密钥交换身份鉴别算法
[R1-ipsec-proposal-1]quit
#R2创建IKE安全提议，与R1配置一致。
[R2] ike proposal 1 //IKE安全提议名称,取值1-15
[R2-ike-proposal-1] encryption-algorithm aes-cbc-128 //密钥加密算法
[R2-ike-proposal-1] authentication-algorithm md5 //密钥交换身份鉴别算法
[R2-ipsec-proposal-1]quit

## Slide 9
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（5）配置IKE对等体，并根据默认配置，配置预共享密钥和两端IP
#R1配置IKE对等体
[R1] ike peer 1 v1 //值串：1-15，STRING<1-15>；版本号：v1/v2
[R1-ike-peer-1] ike-proposal 1 //必须与步骤4的值一致
[R1-ike-peer-1] pre-shared-key simple ipsecvpn //两端密码必须一致
[R1-ike-peer-1] remote-address 12.0.0.2
[R1-ike-peer-1] local-address 11.0.0.1
[R1-ike-peer-1] quit
#R2配置IKE对等体
[R2] ike peer 1 v1
[R2-ike-peer-1] ike-proposal 1
[R2-ike-peer-1] pre-shared-key simple ipsecvpn //两端密码必须一致
[R2-ike-peer-1] remote-address 11.0.0.1
[R2-ike-peer-1] local-address 12.0.0.2
[R2-ike-peer-1] quit

## Slide 10
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（6）配置IKE动态协商方式安全策略，关联上述策略。
#R1关联上述策略
[R1] ipsec policy 1 1 isakmp //ipsec策略值串1-15，次序号1-1000
[R1-ipsec-policy-isakmp-1-1] security acl 3001 //关联ACL,与步骤2一致
[R1-ipsec-policy-isakmp-1-1] proposal 1 //关联proposal策略，与步骤3一致
[R1-ipsec-policy-isakmp-1-1] ike-peer 1 //关联IKE策略，与步骤4一致
[R1-ipsec-policy-isakmp-1-1] quit
#R2关联上述策略，与R1配置一致
[R2] ipsec policy 1 1 isakmp
[R2-ipsec-policy-isakmp-1-1] security acl 3001
[R2-ipsec-policy-isakmp-1-1] proposal 1
[R2-ipsec-policy-isakmp-1-1] ike-peer 1
[R2-ipsec-policy-isakmp-1-1] quit

## Slide 11
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（7）在接口上引用安全策略组，使接口具有IPSec的保护功能
#R1在接口上引用安全策略组
[R1] interface GigabitEthernet0/0/1 //本地路由器出口为引用接口
[R1-GigabitEthernet0/0/1] ipsec policy 1 //与第6步一致
#R2在接口上引用安全策略组
[R2] interface GigabitEthernet0/0/1
[R2-GigabitEthernet0/0/1] ipsec policy 1

## Slide 12
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（8）检查配置结果
配置成功后，在北京总公司的PC1可以ping通上海分公司的PC2，如图10-7所示。但是ping不通Internet路由器，因为Internet路由器没有配置到达R1和R2的路由，如图10-8所示，证明IPSec成功建立。

## Slide 13
10.3.3 IPsec VPN
3． IPSec VPN配置实例
（8）检查配置结果
此时在R1上通过display ipsec sa brief命令查看ipsec安全协商结果，可以看到PC1通过R1出口IP地址11.0.0.1到达PC2入口路由器R2接口IP地址12.0.0.2的数据均被加密传输，加密协议为ESP，加密算法为sha2-256，而且经过对端R2协商成功后才能连接成功，如图10-9所示。